static struct sk_buff *

ieee80211_decap (

struct ieee80211vap *vap, struct sk_buff *skb, int hdrlen)

vap is a pointer to a structure that describes the underlying device.

skb is a pointer to a structure that includes a buffer, where the data of a packet is located. Every packet is associated with an instance of the structure sk_buff.

hdrlen is the length of the header

Returns a new instance of the structure sk_buff that has the data of the previous packet, except for the 80211 frame header. This packet has the appropriate Ethernet header.

I don’t consider about the case of fast frames. So I assume that the constant ATH_SUPERG_FF = 0

- memcpy(&wh, skb->data, hdrlen)

wh (struct ieee80211_qosframe_addr4) keeps the 80211 header of the packet. The function has defined wh in a way that it will be able to keep even the longest frame header.

- llc = (struct llc *) skb_pull(skb, hdrlen)

The function removes the LLC information from the packet. It keeps this information in the variable llc (struct llc).

- Then it uses llc to see if it has to pull more data from the packet and to fill appropriately the variable ether_type.

- eh = (struct ether_header *) skb_push(skb, sizeof(struct ether_header))

The function pushes space for the Ethernet header and eh (struct ether_header) points to this space.

- Then, it fills the two simple fields of the Ethernet header (source and destination) by using the variable wh. Correspondingly to the direction of the message and the 4 or 3 addresses (look Table 2), the function fills the addresses of the Ethernet header.

- Then checks if the pointer to the data is not aligned, and in this case it reproduces an instance of sk_buff.

- It fills the last field of the Ethernet header, eh->ether_type.

- returns the changed skb.